## Slide 1
Dynamic Branch Predictor Using Machine Learning
Aharon Tzur
שנקר - בי"ס גבוה להנדסה ועיצוב

## Slide 2
Scope:
  Modern CPU architectures utilize pipeline processing by staging every command to be handled in several steps such that the clock frequency can be boosted up, which will shorten the overall execution times of programs.
  A branch predictor is required to maximize the successful prediction rate, thus accelerating the program execution.
Description:
Design and implement a pipelined RISC CPU (MIPS Architecture)
Design 2 versions of a branch prediction unit, one of them using machine learning technique (perceptron).
Running sorting programs (benchmarks) and compare the solutions in terms of performance
Introduction

## Slide 3
Use Case

## Slide 4
Engineering design
Top (CPU) – Verilog language
Data Ram
Instruction Ram
Program Counter
ALU
Control Unit
Flush
Register File
Modelsim
(Simulator)
Output Program Assembly language
Branch Predictor
Select PC
Learning Unit
Prediction Unit
IF/ID
ID/EX
Input Program Assembly language
Instructions Assembly language
Simulation results (Monitor)
Test Bench (Verilog + System Verilog)

## Slide 5
Pipeline + Branch Predictor (Architecture)
Clock
Reset
Instruction file
Unsorted Array
Sorted Array

## Slide 6
Branch Predictor – Simple (Architecture)

## Slide 7
Branch Predictor - Perceptron (Architecture)
Prediction Algorithm
Learning Algorithm

## Slide 8
Validation
1. System integrity:
*All the results are for Bubble sort but were test also in selection sort

## Slide 9
Validation
2. Perceptron Hit Ratios With Different History Length:
Expected results are based on Dynamic Branch Prediction Using Machine Learning by Yu Wang & Lei Chen from Department of Computer Science University of California, Davis

## Slide 10
Validation
3. Different size of arrays:

## Slide 11
Issues and their solutions
Predication to normal operation
Negative results to success rate
Path solution for wrong prediction

## Slide 12
Thanks!
Any question?

## Slide 13
Branch Predictor using pipeline:
Example of 4-stage pipeline. The colored boxes represent instructions independent of each other
Branch Predictor - The processor can guess from which branching to bring the following instructions. If it turns out that he chose wrong he cancels the unnecessary calculations. In case of guessing true performance was improved.

## Slide 14
Implementations of Various Predictors:
Perceptron is one basic type of ANN (artificial neural networks) system. A perceptron takes a vector of real valued inputs, calculates a linear combination of these inputs, then outputs 1 if the result is greater than some threshold and 0 otherwise
Prediction with perceptron - The perceptron branch predictor keeps a global history shift register that records the outcomes of branches as they are executed.
Prediction with Bit Priority – with 2-bit branch prediction accuracy (state machine)
Perceptron Diagram block Model
Bit priority block Model

## Slide 15
Predicted Conclusions
Based on Dynamic Branch Prediction Using Machine Learning by Yu Wang & Lei Chen from Department of Computer Science University of California, Davis
Hit Ratios With Different History Length (%) |  |  |  |  |  |  | benchmark | Predictors
L=10 | L=9 | L=8 | L=7 | L=6 | L=5 | L=4 |  | 
59 | 59.7 | 42.5 | 48.6 | 53.8 | 53.8 | 42.3 | Bubble Sort | Perceptron
74.6 | 74.6 | 74.8 | 74.6 | 75 | 74.6 | 74.6 | Bubble Sort | Path - Based
69.3 | 68.2 | 64.4 | 62.3 | 65.1 | 59.1 | 52.9 | Bubble Sort | LVQ

## Slide 16
Assembly code
Address | Data | Comments
0000 | DEAD | This address contains fake data to verify when the address is 0 (for verification only)
0001- 0049 | XXXX | No data
0050 | 0032 | This address contains the array size
0051 | 0000 | This address contains the Iteration
0052 | 0064 | This address contains the first address on the array (100)
0053 | 0095 | This address contains the last address on the array (150)
0054 | 0000 | This address contains the current address in the array
0055 | 0000 | This address contains the next address in the array
0056-0099 | XXXX | No data
0100-0149 | The array | These addresses contain the array
0150-FFFE | XXXX | No data
FFFF | BEEF | This address contains fake data to verify when the address is FFFF (for verification only)

## Slide 17
Branch Predictor (Bit Priority):
LUT 1 – scales for each address
LUT 2 – next address base instruction

## Slide 18
Branch Predictor (Perceptron) + Select PC:

## Slide 19
Flowchart + Instruction set architecture (ISA)

## Slide 20
The registers
Information | Reg Number
The data on the current address | 0
The data on the next address | 1
End address | 2
Size of the Array | 3
The Next Address | 4
The Current address | 5
The Address | 6
The current iteration | 7

## Slide 21
Predication to normal operation – with solution

## Slide 22
Negative results to success rate
count1 = branch instructions counter;
count2 = flush counter;
count3 = skip instructions counter;
count4 = flush (skip instruction only) counter;
Success Rate of all Branch Instructions = (count1 - count2) * 100 / count1;
Success Rate of all Skip Instructions = (count3 - count4) * 100 / count3

## Slide 23
Branch Predictor (Bit Priority) – previous versions
LUT 1 – scales for each address
LUT 2 – next address base instruction

## Slide 24
Data Ram results
Start
Middle
End

## Slide 25
End Simulation

## Slide 26
Conclusion results
count1 = branch instructions counter;
count2 = flush counter;
count3 = skip instructions counter;
count4 = flush (skip instruction only) counter;
Success Rate of all Branch Instructions = (count1 - count2) * 100 / count1;
Success Rate of all Skip Instructions = (count3 - count4) * 100 / count3

## Slide 27
Single Cycle (Architecture)
Clock
Reset
Instruction file
Unsorted Array
Sorted Array